## Slide 1
ATMOSPHERIC INVERSION METHODS
Optimising dyadic basis partitions with stochastic local search
TAC/MHD proof of concept
July 2026

## Slide 2
Basis partitions decide where resolution is spent
A fixed grid treats every location as equally worth resolving.
A data-informed partition can reserve state-vector capacity for regions where footprint–flux sensitivities support it.
fixed grid
adaptive partition
→
Question: can local search improve a useful, physically structured starting partition?
2

## Slide 3
This POC tests one narrow claim
It demonstrates
Deterministic TAC/MHD design construction Proxy-greedy K=32 initialization Stochastic improvement of Gaussian benchmark DFS Reproducible traces and partition visualisation
It does not claim
Posterior inference over partitions An optimal or inferred number of regions A Bocquet-consistent projected prior covariance Production-equivalent observation error treatment
3

## Slide 4
TAC/MHD footprints and CH₄ flux build the design
1
2
3
4
23 MHD + 24 TAC hourly observations
Annual CH₄ flux field
Gᵢc = footprintᵢc × fluxc × 10⁹
Sum-coarsen ×8 47×293×391 → 47×37×49
Benchmark observation covariance
R = diag{max(error, min_error)²}
min_error is a minimum-mismatch floor, not the inferred production total-error process.
Method: demo_data.py; frozen TAC/MHD fixtures under tests/data.
4

## Slide 5
Proxy-greedy splitting creates the K=32 start
For candidate tile v
hᵢᵥ = Σc∈v Gᵢc
sᵥ = (1/aᵥ) Σᵢ Rᵢᵢ⁻¹ hᵢᵥ²
Cells are summed before squaring.
The initializer applies the split with the largest proxy gain until 32 active regions remain.
Background: log(1 + √Σᵢ Gᵢc²/Rᵢᵢ). It is context, not the complete tile score.
Method: initializers.py, objectives.py; visual: tac_mhd_sls.gif.
5

## Slide 6
Fixed-K search changes partition shape
MERGE
One active sibling pair
SPLIT
Another compatible active tile
ACCEPT
Improve, or accept loss L with exp(−L/T)
Gaussian benchmark DFS
D(P) = K − tr[(Bₚ⁻¹ + HₚᵀR⁻¹Hₚ)⁻¹ Bₚ⁻¹]
100
pilot proposals
300
search evaluations
154
accepted moves
Stochastic optimisation, not posterior sampling.
Method: proposals.py, search.py, tac_mhd_sls_manifest.json; DFS inspired by Bocquet, Wu & Chevallier.
6

## Slide 7
Local search improves the Gaussian DFS benchmark
6.6213868511 → 6.6969787847
combined TAC/MHD
2.2306430146 → 2.2599799610
MHD-only diagnostic
4.7197859243 → 4.7464773740
TAC-only diagnostic
Source: tac_mhd_sls_summary.png and tac_mhd_sls_manifest.json. Site-only DFS values are separate, non-additive recomputations.
7

## Slide 8
Full-week data scale variable-K search to 333 observations
FULL-WEEK SCALE-UP
333 hourly rows
165 MHD + 168 TAC
G: 333×293×391 → 333×37×49 No missing-hour imputation 600 evaluations · 366 accepted ≈1 s excluding rendering
U(P) = D(P) − λ max{0, K(P)−32}
Best utility: K=31, DFS=5.8968695574, penalty=0
Start: K=24, DFS=5.8787660714. Final: K=21, DFS=5.8772821075. Same-seed λ response was non-monotone, so λ does not estimate K. GIF/trace retain persistent best DFS separately from best utility.
SELECTED ERROR BENCHMARK
MHD: repeatability combined with within-hour variability. Singleton hours retain zero variability because repeatability remains positive.
TAC: pooled variability; zero pooled variability is replaced by the site median.
Floor selected for all rows: MHD 165/165, 43.210 ppb vs 1.485–26.063; TAC 168/168, 42.863 ppb vs 0.467–16.360. Hourly differences therefore do not affect R.
Source: full-week variable-K summary + manifest; fixed hourly covariance remains non-production.
8

## Slide 9
The covariance is deliberately provisional
CURRENT BENCHMARK
Bₚ = τ² Iₖ
The same isotropic regional covariance is used for every partition.
SCALE-CONSISTENT TARGET
Bₚ = P B Pᵀ
Start from fine-grid covariance B and project it for each partition.
Reusing one numerical Bₚ breaks the Bocquet transformation assumption. The code already accepts a partition-dependent covariance builder, so the search machinery need not change.
Method: objectives.py; covariance design inspired by Bocquet, Wu & Chevallier.
9

## Slide 10
The POC now covers fixed and variable K
WORKING NOW
Dyadic tree + multiscale design Proxy-greedy and random starts Fixed-K paired search (47 rows) Variable-K independent split/merge Full-week 333-row adapter
NEXT EXPERIMENTS
1
Land / sea
Diagnose boundary crossing or impose an explicit constraint
2
Projected covariance
Implement Bₚ=PBPᵀ and compare conclusions
3
Search robustness
Multiple seeds, longer runs, decoupled schedule calibration
4
Posterior integration
Combine partition updates with continuous inference
Status: dyadic_sls_hackathon.md; background: dyadic_partition_inference.md.
10

## Slide 11
TAKEAWAY
The gain persists at full-week scale; K remains unstable.
Next: multi-seed and longer-run robustness, projected covariance, land/sea treatment, and posterior integration.
11